## Slide 1
System Operation Flowchart
Normal sensing cycle and periodic data upload
CONTINUOUS ENERGY PATH
EVERY MINUTE
TEG Array
5 x 1MD06-097-05
Boost Converter
LTC3108-1
Energy Storage
0.22 F Supercapacitor
Buck Converter
Regulated System Supply
RTC Wakes
STM32WLE5
Read ADXL362
Acquire LC76G Fix
Process and Store
Activity + Position
Upload Interval
Reached?
Send Buffered Data
via Integrated LoRa
Return to Stop 2
Wait for Next Cycle
EVERY FEW DAYS
YES
NO
Next scheduled RTC wake-up
Harvest continuously; sense every minute; upload every few days