## Slide 1
System Operation Flowchart
Power conversion path and 1-minute task schedule
POWER PATH
5x TEG Array
1MD06-097-05
Boost Converter
LTC3108-1
Energy Storage
0.22 F Supercapacitor
Buck Converter
Regulated System Supply
Boost charges the storage element; buck conversion supplies a stable rail to the loads below
1-MINUTE TASK FLOW
RTC / MCU
Start Cycle
Read ADXL362
Activity
Acquire LC76G
GNSS Fix
Process and Store
Activity + Position
SX1261 LoRa
Transmission
Return to Sleep
Next 60 s Cycle
Cycle start
0-0.04 s
30-45 s
After GNSS
55 s / 75 ms
Until 60 s
Dashed arrow: RTC starts the next scheduled cycle
Energy is converted and buffered first; sensing, GNSS and LoRa tasks then run sequentially.