## Slide 1
System Operation Flowchart
1-minute sensing cycle | Buffered LoRa upload every few days
ENERGY PATH
TEG Array
LTC3108-1
PMIC
Supercapacitor
Energy Storage
RTC Wake-Up
STM32WLE5
Stored Energy
Above Threshold?
Read Activity
ADXL362
Acquire GNSS Fix
LC76G
Valid Fix Before
Timeout?
Process and Store
Timestamp + Activity + Position
Remain in Stop 2
and Continue Harvesting
Log GNSS Timeout
Keep Previous Valid Position
Upload Interval
Reached?
Transmit Buffered Data
Integrated LoRa
ACK
Received?
Return to Stop 2
RTC Keeps Time
Mark Records Sent
Retain Buffer
Retry Next Upload Window
Continuous charging
YES
NO
YES
NO
YES
NO
YES
NO
Dashed arrows indicate the next scheduled RTC wake-up